Calibration methods for the Surface Scintillator Detector of AugerPrime
UHECR LOGO?
a b
Paul Filip for the Pierre Auger Collaboration
a
b
Karlsruhe Institute of Technology, Institute for Astroparticle Physics, Germany
Observatorio Pierre Auger, Av. San Martin Norte 304, 5613 Malargue, Argentina
 The Pierre Auger Observatory
 AugerPrime detector upgrade
Surface Detector (SD)
~1660 surface detector stations
daily autonomous operation
Detect shower footprint on earth
Multiple detection channels
Cross-calibration via the FD
Facts & Goals
Changes in SD hardware
New SD Electronics
New detection channels
Better sensitivity to primary mass
See talk by D. Schmidt!
Fluorescence Detector (FD)
27 Fluorescence telescopes
Dedicated measurement shifts
Observe longitudinal shower profile
Sensitive to UV light from showers
Surface Scintillator Detector (SSD)
Mounted on top of the water tank
Extruded polystyrene scintillator bars
Sensitive to EM component of shower
Operated in slave mode to water tank
 Offline algorithm
 Motivation & Idea
Building muon histograms
Collect signals with >30 ADC in WCD
Calculate max. pulse height (peak) and integral (charge) for each signal
Log distribution of peaks and charges
Restart process after 61s of acq. time
(uncalibrated) SSD response fluctuates w/ environment
Defines common ground during event reconstruction
Enables monitoring + quantification of detector changes
Enables conceptually simple, but meaningful triggers
Use atmospheric muon signals to calibrate detector
Have sharp muon energy distribution, and good statistics
SSD sensitive to EM
detector deadtimes with increasing rate
WCD filters EM noise effectively
Fitting the muon hump
Muons have characteristic energy deposit
Visible in distribution of peak and charge
Fit parabola to distribution, vertex is the most probable peak (charge) of an omni- directional through-going muon
 Online algorithm
Ulbricht sphere as diffuse emitter
NIST-calibrated LED (λ = 365 nm)
Portable (fits in carry-on luggage)
Calibration of source on- and off-site
 Horizontal vs. Omnidirectional MIP