Towards an online MIP calibration

---
Current (WCD) calibration
- WCD offline calibration
  - Fit muon hump in histogram
- WCD online calibration
  - Calibration trigger with threshold , that satisfies:
    - Threefold coinc. of
    - >1 PMT above
  - Iteratively adjust threshold until 70 Hz rate is reached
  - Threshold equals
  - Accurate to ~2%
  - See also GAP2023-049
color rgb 128 128 128 {k}
color rgb 128 128 128 { asd }
Streich 2022
color rgb 128 128 128 { 2.5 I_"VEM" " cut"} newline color rgb 128 128 128 {"~70 Hz rate"}
color rgb 128 128 128 {1.0 k}
color rgb 128 128 128 {k approx 2.5 I^"WCD"_"Peak"}
omnidirectional muon hump
~
color rgb 128 128 128 { ~1.15 I_"VEM" }
change in binning

---
Setting up rate/threshold relationship
- 870,000 SSD histograms from SD-1500 T3s in Jun/Dec 2023
- Bootstram muon events according to SSD histogram to estimate
color white{ I^"SSD"_"histo" }
- Characteristic shape
- Scale differs due to gain
- determined by:
  - Weather
  - Electronics
  - ???
- Does there exist a stable rate/threshold relationship?
color white { I_"MIP" }

---
MIP → Rate
color white{ I^"SSD"_"histo" }
- Fit parabola to histogram to obtain
- For threshold in {1.00, …, 5.00} :
  - count entries above given threshold
  - Per station: remove outliers at 3σ
  - Per station: take mean of samples
  - Divide by histogram acquisition time
  - Average across all stations
- Systematic: station-to station fluctuations ~20%
- Statiscical: Poisson error on counts above threshold
color white{ I^"SSD"_"histo" }

---
MIP ← Rate
color white{ t }
- Adjust threshold of SB trigger until until rate converges to Hz
- given as (read off , from plot)
- Compare	to “true”
color white{ f }
color white { I^"SSD"_"rate" }
color white{ kt }
color white{ f k }
color white { I^"SSD"_"rate" }
color white { I^"SSD"_"histo" }

---
MIP ← Rate
color white{ t }
- Adjust threshold of SB trigger until until rate converges to Hz
- given as (read off , from plot)
- Compare	to “true”
color white{ f }
color white { I^"SSD"_"rate" }
color white{ kt }
color white{ f k }
color white { I^"SSD"_"rate" }
color white { I^"SSD"_"histo" }

---
MIP ← Rate
color white{ t }
- Adjust threshold of SB trigger until until rate converges to Hz
- given as (read off , from plot)
- Compare	to “true”
- Best correlation at intermediate values
- Large sampling error at very high values
color white{ f }
color white { I^"SSD"_"rate" }
color white{ kt }
color white{ f k }
color white { I^"SSD"_"rate" }
color white { I^"SSD"_"histo" }