Towards an online MIP calibration

---
Current (WCD) calibration
- WCD offline calibration
  - Fit muon hump in histogram
- WCD online calibration
  - Calibration trigger with threshold , that satisfies:
    - Threefold coinc. of
    - >1 PMT above
  - Iteratively adjust threshold until 70 Hz rate is reached
  - Threshold equals
  - Accurate to ~2%
  - See alsp GAP2023-049
color hex 999999 {k}
color rgb 128 128 128 { 2.5 I_"VEM" " cut"} newline color rgb 128 128 128 {"~70 Hz rate"}
Streich 2022
color hex 999999 {0.7 k}
color hex 999999 {1.0 k}
omnidirectional muon hump
~
color rgb 128 128 128 { ~1.15 I_"VEM" }
color hex 999999 {k approx 2.5 I_"VEM"}
change in binning

---
Setting up rate/threshold relationship
- 870,000 SSD histograms from SD-1500 T3s in Jun/Dec 2023
- Bootstrap muon events according to histo to estimate
color hex 999999 {I^"SSD"_"histo"}
- Characteristic shape
- Scale differs due to gain
- determined by:
  - Weather
  - Electronics
  - ???
- Does there exist a stable rate/threshold relationship?
color hex 999999 {I_"MIP"}

---
MIP → Rate
- Fit parabola to histogram to obtain “true”
- For threshold in {1.0, …, 5.0} :
  - Count histo entries above
  - Per station: remove outliers at 3σ
  - Per station: take mean of samples
  - Divide by histogram acquisition time (61s)
  - Average across all stations
- Systematic: station-to-station fluctuations ~20%
- Statistical: Poisson error on counts above threshold
color hex 999999 {t}

---
MIP ← Rate
- Adjust threshold [ADC] of SB trigger until rate converges to Hz
- given as (read off , from plot)
- Compare and “true”
color hex 999999 {f}
color hex 999999 {I^"SSD"_"rate"}
color hex 999999 {kt}
color hex 999999 {k f}
color hex 999999 {I^"SSD"_"rate"}

---
MIP ← Rate
- Adjust threshold [ADC] of SB trigger until rate converges to Hz
- given as (read off , from plot)
- Compare and “true”
- Stron EM influence at low thresholds
- Best correlation at intermediate values
- Large sampling error at very high thresholds
color hex 999999 {f}
color hex 999999 {I^"SSD"_"rate"}
color hex 999999 {kt}
color hex 999999 {k f}
color hex 999999 {I^"SSD"_"rate"}